Water safety plans for piped urban supplies in developing countries: a case study from Kampala, Uganda

GUY HOWARD, SAM GODFREY, SARAH TIBATEMWA and CHARLES NIWAGABA

Department for International Development (DFID), United House, 10 Gulshan Avenue, Gulshan 1,

Dhaka 1212, Bangladesh Water, Engineering and Development Centre (WEDC), Loughborough University, Leicestershire

LE11 3TU, UK

§National Water and Sewerage Corporation, Jinja Road, Kampala, Uganda Public Health and Environmental Engineering Laboratory, Department of Civil Engineering,

Makerere University,Kampala, Uganda

Abstract

The World Health Organisation (WHO) promote the use of water safety plans (WSPs) in the 3rd edition of the Guidelines for Drinking-Water Quality (2004). WSPs place an emphasis on risk assessment coupled with risk management, with simple indicators to monitor process control and periodic verification through audit and microbial indicators. A WSP was developed for the Kampala piped water supply in Uganda by the National Water and Sewerage Corporation. The use of risk maps was found to greatly aid the identification of hazardous events in the distribution system. A validation exercise was performed that showed the WSP was properly designed. The study shows WSPs can be successfully developed for utilities in developing countries and offer significant cost savings in water quality control. Senior management endorsement was found to be essential to provide the authority to develop and implement the activities required for effective water safety management.

Keywords: Water safety plans; Developing countries; Utilities