Experiences on the implementation of a pilot grey water treatment and reuse based system at a household in the slum of Kyebando-Kisalosalo, Kampala

Charles B. Niwagaba, Patrick Dinno, Isaac Wamala, S. Sahar Dalahmeh, Cecilia Lalander and Håkan Jönsson

Abstract

Grey water constitutes the largest fraction of domestic wastewater. It causes environmental sanitation and pollution problems if it is not managed well. If treated, grey water can be a resource for a variety of uses. A pilot system was constructed in February 2013 to treat grey water from a fourmember household for sub-surface irrigation of local vegetables. A hydraulic loading rate (HLR) of 60 L m-2 d-1 and an organic loading rate (OLR) of 519–1,580 g BOD5m-2 d-1 were implemented on a multi-media filter of gravel, charcoal, geotextile and mulch (charcoal being the predominant layer) operated as a batched type-system, with a 36-hour retention time. The system was operated for three months, during which it showed remarkable removal efficiencies of 90.8±5.4 and 96.1± 3.0% after 36 hours for COD and BOD, respectively, and 95±3.1% for faecal coliforms (FC). The removal efficiencies at 36 hours, of total nitrogen (TN), total phosphorus (Tot-P), total suspended solids (TSS) and total dissolved solids (TDS) were 39.0, 30.1, 85.2 and 78.6%, respectively. Plant response to subsurface irrigation with treated grey water was largely masked by rainy season and the effluent had a limited effect on the soil.

Key words | grey water, household, reuse, sub-surface irrigation, treatment